## Slide 1
ENGINEERING OVERVIEW
STM32F411
SMBus / I2C
USB Adapter
An open firmware and host stack for controller, addressed-slave, SMBus, and MCTP transactions over USB.
Project architecture • API surface • integration examples
HOST
USB
STM32
F411
TinyUSB + I2C1
TARGET
I2C / SMBus
Notes: [Sources]
- README.md
- middleware/usb/usb_device.c
- drivers/i2c.c

## Slide 2
STM32F411 SMBUS / I2C USB ADAPTER
One adapter supports three bus workflows
02
01
I2C controller
Scan 7-bit addresses, select 100 or 400 kHz, write up to 507 bytes, and read up to 509 bytes with detailed status.
DEVELOPMENT & DEBUG
02
Addressed slave
Listen on a configurable address, poll asynchronously, and retrieve up to four queued external-master writes.
EMULATION & TEST
03
SMBus + MCTP
Issue 1–32 byte raw/block operations or exchange 4–256 byte MCTP packets with PEC handled in firmware.
PLATFORM MANAGEMENT
Notes: [Sources]
- README.md
- protocol/usb_protocol.h
- middleware/adapter/adapter_service.h

## Slide 3
STM32F411 SMBUS / I2C USB ADAPTER
Hardware needs USB, three bus wires, and pull-ups
03
HOST PC
libusb client
CLI or application
STM32F411CEU6
Black Pill
PA11 USB D−
PA12 USB D+
PB8 I2C1 SCL
PB9 I2C1 SDA
I2C / SMBus
TARGET
3.3 V logic
common ground
USB FS
SCL / PB8
SDA / PB9
GND
≈4.7 kΩ
≈4.7 kΩ
External pull-ups to 3.3 V are required on both SCL and SDA.
Notes: [Sources]
- README.md
- drivers/i2c.c
- middleware/usb/usb_device.c
- middleware/usb/usb_descriptors.c

## Slide 4
STM32F411 SMBUS / I2C USB ADAPTER
Four layers carry every USB request
04
Host client
Discovery
libusb bulk I/O
CLI argument handling
main.c
USB protocol
16-byte header
sequence + opcode
≤512-byte payload
usb_protocol.c
Adapter service
Validation
mutex + status mapping
async event state
adapter_service.c
Bus engines
I2C1 master/slave
SMBus block write
MCTP transport + PEC
i2c.c / mctp_smbus.c
FreeRTOS serializes shared I2C access; TinyUSB runs the vendor interface on endpoint 0x01 OUT / 0x81 IN.
Notes: [Sources]
- host/usb_client/main.c
- middleware/usb/usb_protocol.c
- middleware/adapter/adapter_service.c
- drivers/i2c.c
- middleware/mctp/mctp_smbus.c

## Slide 5
STM32F411 SMBUS / I2C USB ADAPTER
The current host deliverable is a CLI, not a library
05
CURRENT REPOSITORY
smbus-usb
Mach-O ARM64 executable
Links to libusb-1.0.dylib
Auto-discovers the first free adapter
Implements every documented command
RECOMMENDED PACKAGE
libsmbus_usb.so
Move transport and API calls into a stable C ABI. Keep the CLI as a thin wrapper. Publish Linux .so, macOS .dylib, headers, versioning, and examples from one source tree.
Why this matters
Direct integration from C/C++, Python ctypes, test frameworks, and manufacturing tools.
Notes: The `.so` requested for this presentation was not present in the inspected folder. This slide separates verified current state from the proposed packaging improvement.
[Sources]
- host/usb_client/Makefile
- host/usb_client/main.c
- host/usb_client/adapter_discovery.c
- host/usb_client/smbus-usb

## Slide 6
06
Applications
C / C++
Python ctypes
CI and factory tools
Shared library
open / close
detect / bitrate
read / write / MCTP
libusb
VID/PID discovery
claim interface 0
bulk IN / OUT
STM32 firmware
validate frame
dispatch opcode
execute bus operation
Design rules
Opaque handle • explicit timeouts • thread-safe calls • versioned structs • transport status separated from I2C status
STM32F411 SMBUS / I2C USB ADAPTER
One ABI serves every host language
Notes: This is a proposed packaging boundary based on the existing CLI implementation; it is not yet present in the repository.
[Sources]
- README.md
- protocol/usb_protocol.h
- host/usb_client/main.c

## Slide 7
STM32F411 SMBUS / I2C USB ADAPTER
One API spans every adapter workflow
07
DISCOVER & CONFIGURE
find_devices
i2c_detect
i2c_bitrate
enumerate • scan • 100/400 kHz
CONTROLLER I/O
i2c_write
i2c_write_ext
i2c_read_ext
0–507 B write • 1–509 B read
ADDRESSED SLAVE
i2c_slave_enable
async_poll
i2c_slave_read_ext
256 B TX • 258 B RX • FIFO depth 4
SMBUS & MCTP
smbus_read
smbus_write
mctp_send_receive
1–32 B SMBus • 4–256 B MCTP
USB DIAGNOSTICS
ping
info
echo
selftest
framing tests through 512-byte payload
Notes: [Sources]
- README.md
- protocol/usb_protocol.h
- middleware/adapter/adapter_service.h

## Slide 8
08
01 FRAME
SMBA magic
version + opcode
sequence + length
02 TRANSFER
Bulk OUT 0x01
USB packets are not
message boundaries
03 EXECUTE
Validate request
lock I2C1
run selected service
04 RETURN
Bulk IN 0x81
repeat opcode + sequence
status + payload
16-byte header
Maximum protocol payload: 512 bytes • multi-byte fields: little-endian • detailed I2C status lives inside extended-response payloads
STM32F411 SMBUS / I2C USB ADAPTER
One path handles every operation
Notes: [Sources]
- protocol/usb_protocol.h
- middleware/usb/usb_protocol.c
- host/usb_client/main.c

## Slide 9
STM32F411 SMBUS / I2C USB ADAPTER
One adapter supports six practical workflows
09
Board bring-up
Scan a new board, confirm pull-ups and addressing, then perform basic reads and writes.
Sensor / EEPROM access
Exercise register maps, configuration bytes, and data acquisition from scripts or test tools.
Slave emulation
Receive controller writes at a chosen address and validate firmware behavior against an emulated endpoint.
Automated production test
Embed the shared library in fixtures for deterministic device discovery and pass/fail reporting.
MCTP endpoint debug
Send request packets over SMBus, validate PEC, and inspect the complete returned transport packet.
USB transport diagnosis
Use ping, info, echo, and selftest to isolate USB framing from external bus problems.
Notes: [Sources]
- README.md
- middleware/adapter/adapter_service.c
- middleware/mctp/mctp.c

## Slide 10
STM32F411 SMBUS / I2C USB ADAPTER
Five commands prove host-to-bus operation
10
# Build the host client
make host
# Prove USB framing and discover targets
./host/usb_client/smbus-usb ping
./host/usb_client/smbus-usb i2c_detect
# Select fast mode and exercise address 0x50
./host/usb_client/smbus-usb i2c_bitrate 400000
./host/usb_client/smbus-usb i2c_write_ext 0x50 0 0x00
./host/usb_client/smbus-usb i2c_read_ext 0x50 0 16
Expected checkpoints
PONG
USB framing is alive
0x50
Target acknowledged during scan
status=0
Extended transaction succeeded
Register semantics depend on the connected target; use its datasheet for the command sequence.
Notes: [Sources]
- README.md
- host/usb_client/main.c
- host/usb_client/Makefile

## Slide 11
STM32F411 SMBUS / I2C USB ADAPTER
The proposed library keeps application code compact
11
PROPOSED ABI — illustrative until the .so and header are added
smbus_handle_t *adapter = NULL;
uint8_t ports[8];
uint8_t rx[16];
size_t count = smbus_find_devices(ports, 8);
if (count > 0 && smbus_open(ports[0], &adapter) == SMBUS_OK) {
smbus_i2c_bitrate(adapter, 400000);
smbus_i2c_write_ext(adapter, 0x50, 0, tx, tx_len, &written);
smbus_i2c_read_ext(adapter, 0x50, 0, rx, sizeof(rx), &read);
smbus_close(adapter);
}
ABI expectations
• Opaque adapter handle
• Explicit buffer lengths
• Separate USB and I2C results
• No global mutable state
• Stable symbol versioning
• Linux .so + macOS .dylib
Names shown here are a design recommendation, not verified exports from a supplied binary.
Notes: Proposed C ABI. The repository does not currently supply a shared-library header or binary to verify symbol names.
[Sources]
- README.md
- host/usb_client/main.c
- host/usb_client/adapter_discovery.h
- protocol/usb_protocol.h

## Slide 12
NEXT STEP
Package the proven transport as a supported host SDK
1 Extract transport + commands into libsmbus_usb
2 Publish header, .so / .dylib, examples, and ABI tests
3 Replace development VID/PID and document platform permissions
4 Add CI hardware tests for 100/400 kHz, NACK, timeout, slave FIFO, and MCTP
Current engineering risks
No shared library in folder • development VID/PID • only 7-bit / no-flags operations • slave read data fixed to 0xFF until a response API is added
Notes: [Sources]
- README.md
- host/usb_client/Makefile
- middleware/usb/usb_descriptors.c
- drivers/i2c.c